Potential 2D Flows of Real Gases. Invariant Equations in Natural Coordinates. Hodograph Transformation

Ernest G. Shifrin

Moscow Institute of Physics and Technology, Institutski str. 9, Dolgoprudny, Moscow region, 141700, Russia

ernest-shifrin@yandex.ru

Abstract

We consider plane-parallel and axially symmetric stationary potential flows of real gases. We deduce the motion equations in the natural coordinates that are invariant with respect to thermodynamic state laws. This allows to extend, almost with no change, methods of classical gas dynamics to a broad class of urgent problems. We generalize the Chaplygin transformation onto flows of real gases (combustion gases, superheated steam etc.). In particular, this will allow to apply our method of aerodynamic designing for precise constructing gas and steam turbines as well as jet nozzles.

The obtained equation in the Chaplygin variables differs from the classical one only by the coefficients that depend on concrete thermodynamic laws. The equation of axially symmetric flows has in addition right-side part that contains the transformation's Jacobian.

Keywords: Gas dynamics, aerodynamic designing, real gas, hodograph, 2D-flows, first integral, stationary, potential, stream function, separated-free, Chaplygin's equation, well-posed problem.

Introduction

Plane-parallel and axially symmetrical potential flows of an real gas take place in diverse technical devices. In this work, we specify and expand results of our work [1], bearing in mind mainly the problem of aerodynamic designing. As the most important employments we mean flows of the superheated steam and products of fuel combustion in turbines, as well as in nozzles of rocket engines. In these devices dissociation takes place because of high temperature, therefore a quality designing cannot be attained without taking into account real nature of gases.

When designing gas dynamic device, they are searching such form of a body that provides a steady, separation-free flowing. As a rule, this problem is being solved by selection of suitable solutions of the direct problem defined on a set of close bodies. (This problem consisting in determination of the flow around a given body is assumed to be uniquely solvable.) However the hard condition for the flow to be separation-free requires rather thin adjustment of search strategy. Therefore this approach is not always successful.

In the book [2] we have developed another method of aerodynamic designing based on the hodograph-transformation of potential 2D-flows of a perfect (Clapeyron's) gas. This transformation has turned out extremely useful since transition to the velocity variables has made the designing problem well-posed. Firstly, hodograph-image of the flow domain can be set enough arbitrarily. This makes possible to satisfy in advance the condition for the velocity distribution along a body to be increasing (or not too strongly decreasing). By the boundary layer theory [3] this provides a separation-free flow at any Re number and consequently guarantees adequacy of the mathematical model of ideal gas. Secondly, the designing problem can be formulated for the Chaplygin equation as well-posed one.

Initially this method has been employed for designing contours of the Laval nozzles of supersonic aerodynamic tubes [2]. Namely, the shortest nozzles with angular points at intersections of the contours with the rectilinear sonic lines have been constructed. These nozzles were manufactured and are in exploitation in Russia since 1980; the checking has shown that non-uniformity in the Mach number in these tubes does not exceed 1%.

After that the following devices have been designed:

a lattice of the turbine nozzle guide vanes [4]

an subcritical lifting wing section for flight with high subsonic velocity [5]

an inlet valve of a piston engine [6],[7]

a ring-shaped Laval nozzle [8].

Now, to expand the method scope, we deduce invariant equations of imperfect non-barotropic gases in the physical and hodograph variables. (Hodograph-mapping of plane-parallel flows of barotropic gases was described by R.Mises [9].)

First integrals of stationary 3D-flows of inviscid fluids

In this section we specify some results given in the monograph [9], Chapter V. (Adiabatic flow of inviscid fluid).

By definition, a first integral is an explicit expression satisfying a differential equation. Using first integrals, one can simplify mathematical problem.

From view point of the classical mechanics, homogeneous gas is a two-parametric locally-balanced thermodynamic medium: all thermodynamic parameters (the temperature , pressure , density , interior energy  and so on) obey classic thermodynamics and can be expressed via any two of them [10]. We choose entropy  and enthalpy  as independent variables. By  denote the ratio . We consider the differentiable functions  and  as laws of the thermodynamic state. We write down the first law of thermodynamics as follows

(1)

The thermodynamic sound velocity  is determined by the formula

(2)

It follows from eq.(1)

Substituting this formula into eq. (2), we obtain

(3)

Therefore eq.(1) takes the form

(1')

A stationary 3D-flow of an ideal imperfect gas obeys the equations

Here  is a flow velocity, . The functions  are defined by thermodynamics of an real (imperfect) gas.

The full temperature  and entropy in the Clapeiron gas are known to be constant on stream lines. The analogous property takes place in imperfect gas.

(By definition, the stream lines are vector lines of the velocity field .)

Theorem 1. System (4) has two first integrals: entropy  and "full enthalpy"  are constants on stream lines, i.e. .

Proof. First transform the energy equation using the continuity equation

(5)

Now consider the momentum equation

Multiplying on  and taking into account eq.(5), we obtain

Comparing with eq.(1) written in the form

we obtain that . Theorem 1 is proved.

Theorem 2. Let us suppose that: (i) vectors  and  are not collinear in Q and  (ii) identically. Then  if and only if .

Proof. Let  be arbitrary unit vector, . It follows from eq. (1') that

Using formula (3), we obtain

(6)

Taking scalar product of the momentum equation and the vector , we obtain

Taking into account the condition (i) and comparing with eq.(6), we have

By virtue of arbitrariness of vector  it follows from here that . Therefore if , then  and  are collinear, consequently we obtain

This contradicts to the condition (ii). Theorem 2 is proved.

Invariant form of equations of 2D-potential flows

Transform system (4),(5) for plane-parallel (N=0) and axially symmetrical (N=1) potential flows. Let the potential  and stream function  form curvilinear orthogonal coordinate system . Here  are unit vectors of Cartesian coordinate system  combined (in the axially symmetric flow) with the symmetry axis . In correspondence with the Theorem 2 we have

Let us denote . By  denote  rotated on  counter-clockwise. If , then

By  denote directional derivatives. In the points, where  the first equation of system (4) can be transformed to the form

Differential geometry says that

where . By virtue of the Meusnier theorem we have

(7)

By  denote the Mach number. It follows from eq.(1')  that at  																			 			(8)

Using eqs.(7),(8), we obtain

(9)

Taking the scalar products of the second equation (4) with  and bearing in mind that , we have

(10)

(11)

Eqs. (9),(10),11) can only be considered locally, as they involve directional rather than partial derivatives. Denoting by  the Lame coefficients, we have

(12)

By virtue of the Theorem 2 we have 																	 			  (13)

It follows from the comparison of the equality  with eq.(11) that . Calculating , we obtain that

Using eqs.(12) we express finally the invariant form of equations of potential flows written in the natural coordinates

(14)

Here dependence on thermodynamics is determined only by eqs. (13).

Invariance of eq. (14) consists in that that they do not differ formally from those for Clapeiron's gas. However unlike Clapeiron's gas, in which , the sound velocity  cannot be expressed via density . Therefore so called "replacement principle" [9],[11] does not hold in imperfect gases even in potential flows. In other words, relational positioning of stream lines and level lines of velocity depends on constants .

Hodograph transformation

In plane-parallel flows eqs.(14) are homogeneous with respect to derivatives, therefore changing  can be made without trouble by using formulas of type

However for axially symmetrical flows this approach is impossible as obtained expressions cannot be cancelled by the Jacobian. 	Therefore we apply here another approach, which we have used while designing axially symmetrical supersonic aerodynamic tubes [2] and an inlet valve of the piston engine [12].

Let us write equations of stationary potential flows down

(15)

Differentiating, we obtain

(16)

where .

Let us change places of dependent and independent variables. Denoting by  the Jacobian ) we have

(17)

Substituting formulas (16) into eqs.(15) we obtain

It follows from first eq. (15) that

(18)

Resolving system (6),(7) with respect to derivatives , we have

(19)

Cross-differentiating the expressions for  and , we obtain the equation for the stream function  with the Chaplygin operator on its left-hand side

(20)

The Jacobian  is also expressed via derivatives  and . Indeed, substituting expressions (18) into equality , we obtain

Keeping in mind that

we transform eq.(20) to the final form

(21)

Here , where  are determined by eq.(13). We have

(22)

(23)

The problem of aerodynamic designing is formulated as a boundary problem for eqs.(21)-(23) in some domain in the hodograph plane. Integrating expressions (19) for , we carry out the mapping into physical plane. Arbitrariness of the flow domain allows to optimize device being designed.

Acknowledgements

This work is supported by the federal target program of the Ministry of Education and Science of the Russian Federation called ”Research and development on the priority directions of scientific-technological complex of Russia for 2014-2020”, unique identifier for Applied Scientific Research: RFMEFI57814X0048.

References

[1] 	Shifrin E.G., 2006, "Two-dimensional stationary vortex flows of an ideal imperfect gas in natural coordinates", Doklady Physics, 51(11), pp. 625-629.

[2] 	Shifrin E.G., and Belotserkovskii O.M., 1994, "Transonic vortical gas flows", John Wiley & Sons.

[3] 	Olejnik O.A., 1969, "Mathematical Problems of Boundary Layer Theory: Lecture Notes, Spring Quarter", University of Minnesota, Department of Math.

[4] 	Shifrin E.G., and D.S.Kamenetskii, 1993, "Application of the hodograph method to nozzle guide vane profiling", Russian Journal of Computational Mechanics, 3, pp. 80-107.

[5] 	Shifrin E.G., and Alferov S.A., 1999, "The carrier subcritical profile for a high subsonic velocity of flight", Doklady Physics, 44, pp.779-783.

[6] 	Pelevin O.V. and Shifrin E.G., 1999, "Profiling the contour of an intake valve in an internal combustion engine by the hodograph method", Computational mathematics and mathematical physics. 6, pp.1023-1031.

[7] 	Shifrin E.G., and Korneev B.A., 2014, "The aerodynamic design of the inlet channel of the four-stroke engine". IJAER, V.9, 23. pp.21003-21016.

[8] 	Shifrin E.G., and Kim Ch.V., 2005, "Shaping a nozzle with a central body by the Chaplygin method", Doklady Physics. 50(3), pp.143-146.

[9] 	Mises R., 1958, "Mathematical theory of compressible fluid flow", Academic Press, NY.

[10] 	Germain P., 1973, "Cours de Me'canique des Milieux Continus", Masson et Companie, Paris.

[11] 	Munk M., and Prim R.C, 1947, "On the multiplicity of steady gas flows having the same streamline pattern", Proc. Nat. Acad.Sci. USA, 33, pp.137-141.